## Slide 1: Full-custom and mixed signal design tutorial - V0.2
SS65 PDK

## Slide 2: History
V0.1 - release on 02-Jan-2017 - by trangdld
V0.2 - release on 21-Feb-2017 - by trangdld

## Slide 3: Content
Server access and account setup
SS65 PDK and design tools introduction
Full-custom design
  Schematic
  HSPICE simulation
  Layout
  Verification: DRC, LVS
  Parasitic extraction and post-simulation
Digital design
  Digital design synthesis
  Digital simulation
  Pad insertion
  Place and Route
  Error handle
Mixed-signal design
  Preparing
  PnR
  Layout integration
  Chip merger (머지)
Stream in/out

## Slide 4: Download tools from IDEC ftp server
wget -r --user="cadtmp" --password=‘\!cadtmp11?' ftp://143.248.230.149/CADENCE/IC616/Linux/
tool directory that you need

## Slide 5: 1. Server access and account setup
SS65 is a secure server, that is accessed by Power server
From Windows PC, using Xshell to connect to Power server
From Linux PC, use command: ssh -X -p 32722 {user_name_on_Power_server}@163.180.118.55
User
Power server
163.180.118.55:32722
SS65 server
10.8.0.1
Tools
SS65 PDK
License servers
(contact admin for detail)
Any name
Click OK to connect

## Slide 6: 1. Server access and account setup
From Power server, using ssh command to connect to SS65 server:
ssh -X {your_user_name_on_SS65}@10.8.0.1
Change to csh mode: csh
in the working directory, set environment variables: source l6lp.env
l6lp.env is script file that contains Environment variable for using SS65 PDK and the related tools
New account
cds.lib is script file that define libraries of SS65 for Virtuoso library manager

## Slide 7: 1. Server access and account setup
in the working directory, make a l6lp.env file
Modify the paths for compatibility if need.
########## SEC L6LP Environment ###################################
setenv LANG C
setenv CDS_Netlisting_Mode "Analog"
setenv DEVICELIB_ROOT /Tools/Library/MPW126/pdk_analog/S65/SS65/sec120209_0007_LR6LP_PDK_PROC_PDK_N/PDK/NORMAL/LR6LP_CDS_V1.5.0.12_SEC3.5.3.8/SEC_CDS/l6lpdk/V1.5.0.12_SEC3.5.3.8
setenv CDS_INST_DIR /Tools/Cadence/IC615
setenv CDS_AUTO_64BIT ALL
setenv SPECTRE_FEATURE_FILE /Tools/Cadence/MMSIM121/tools/spectre/etc/files/spectre.dat
#setenv XCAL_MAXD_MODE smart
#setenv PEX_RUN TURE
#setenv PEX_CORNER NORMINAL
set path = ($CDS_INST_DIR/tools/bin $CDS_INST_DIR/tools/dfII/bin $path)
source /Tools/Library/MPW126/pdk_analog/S65/SS65/SECPDK/LR6LP/REV00/rule/DRC/CalibreDRC/L6LP_CalibreDRC_V1.5.0.5_SEC1.1.0.30/DRC/sourceme_v1505.65lp
source /Tools/Library/MPW126/pdk_analog/S65/SS65/SECPDK/LR6LP/REV00/rule/PEX/CalibreXRC/CalibreXRC/XRC/LR6LP_xRC_Calibre_V1.5.0.9_SEC0.0.0.13/sourceme
source /Tools/Library/MPW126/pdk_analog/S65/SS65/SECPDK/LR6LP/REV00/rule/LVS/CalibreLVS/CalibreLVS/LVS/L6LP_CalibreLVS_V1.5.0.9_SEC0.0.0.22/sourceme
setenv HSP_HOME /Tools/Synopsys/Hspice/hspice
setenv META_QUEUE 1
#source $HSP_HOME/bin/cshrc.meta
set path=($HSP_HOME/amd64 $HSP_HOME/bin $path)

## Slide 8: 1. Server access and account setup
in the working directory, make a cds.lib file
# Default Library Define
DEFINE basic $CDS_INST_DIR/tools/dfII/etc/cdslib/basic
DEFINE analogLib $CDS_INST_DIR/tools/dfII/etc/cdslib/artist/analogLib
# Sample cds.lib file for the Cadence Design Framework II
# Set environment variable DEVICELIB_ROOT to installation path(l6lp.env in env directory)
# of the devicelib package.
# Important: Select the library of the desired BEOL layer stack
# SEC L6LP Library Define
DEFINE l6lp $DEVICELIB_ROOT/oa/l6lp
# SEC LR6LP Library Define for RF process
DEFINE lr6lp $DEVICELIB_ROOT/oa/lr6lp
# Technology Library
DEFINE l6lp_tech $DEVICELIB_ROOT/oa/l6lp_tech_4_20_01_00

## Slide 9: 1. Server access and account setup
1 error in hosts setup make virtuoso fail: wrong ip order
127.0.0.1 vlsi-dist.khu.ac.kr localhost localhost.localdomain localhost4 localhost4.localdomain4
163.180.118.162 License_Server
163.180.118.162 License_Server
127.0.0.1 vlsi-dist.khu.ac.kr localhost localhost.localdomain localhost4 localhost4.localdomain4
corrected order

## Slide 10: 2. SS65 PDK and design tools introduction
Schematic and layout: Virtuoso
spice simulation: HSPICE
DRC, LVS, PEX: Calibre (integrated in virtuoso)
Front-end digital design synthesis: Design Compiler (DC)
Back-end: IC Compiler (ICC)
SS65
Analog
Standard cell
Memory
(SRAM)
IO
Samsung
IDEC
MPW service
CSAVLSIKHU

## Slide 11: 3. Full-custom design
  Schematic
  HSPICE simulation
  Layout
  Verification: DRC, LVS
  Parasitic extraction and post-simulation
Design example: RC oscillator

## Slide 12: 3.a. Schematic with Virtuoso
in the working directory:
virtuoso &
In Library Manager: File/New/Library
Make your own library “RORC” then click OK
Select “Reference …”
Choose “l6lp” then OK

## Slide 13: 3.a Schematic
In library, select RORC
File/New/Cell Views
add Cell name: Schmitt_trigger
View schematic, then OK
Schematic Editor window will appear
Click to “Save and check”

## Slide 14: 3.a Schematic
In Schematic Editor: Add Instance by press key “i“
In Add Instance: click Browse then choose “l6lp” library.
Select cell “nfet” for NMOS and “pfet” for PMOS in RVT or “lvtnfet”/”lvtpfet” in LVT. Select View symbol.
Click back to Schematic Editor window to paste the instance
the instance’s properties can be change here or in Properties windows later
RVT: regular voltage
LVT: low voltage

## Slide 15: 3.a. Schematic
Some basic key in Sch. Editor:
  i : add Instance
  w: wire connecting
  l: assign label for net
  p: add port
  q: open Properties of an instance
  m: move
  d: delete
  esc: cancel command
  u: undo
After finish the schematic, click “save and check” for saving and checking your design. It should be no error or warning.
Make symbol: Create/Cellview/From Cellview  OK

## Slide 16: 3.a. Schematic
Symbol option recommend:
  Left Pins: input signals
  Right: output signals
  Top: Power
  Bottom: Ground, reset

## Slide 17: 3.a. Schematic
In higher hierarchical design, we make RO cell
in designing, some properties are frequent changed so they should be name as parameters. So, later, their value can be modified easily in HSPICE simulation.

## Slide 18: 3.b. HSPICE simulation
Export HSPICE netlist from the schematic:
  from Schematic Editor (RO sch), launch ADE L
  in ADE L, Setup/Simulator. Choose hspiceD, then OK
  in ADE L, Simulation/Netlist/Create to create HSPICE netlist.
  in Netlist window, File/Save as. Save the netlist in HSPICE working directory.

## Slide 19: 3.b. HSPICE simulation
make a new hspice file, named as RO.sim.sp
Add library to hspice tcl file: .lib "/Tools/Library/MPW126/pdk_analog/S65/SS65/SECPDK/LR6LP/REV00/model/HSPICE/LR6LP_Hspice_V1.5.0.9_SEC2.2.6.1/HSPICE_netlist.lib" FF
  Condition: NN, FF, SS, FS, SF, or MONTE
run HSPICE: hspice64 RO.sim.sp

## Slide 20: 3.b HSPICE simulation
for browser the simulation result (waveform), in ADE L window, choose Tools/Results Browser  Virtuoso Visualization and Analysis XL window: File/Open results

## Slide 21: 3.c. Layout
CMOS layout

## Slide 22: 3.c. Layout
CMOS layout

## Slide 23: 3.c Layout
Display resources: CIWToolsDisplay Resources
Merge  OK  close

## Slide 24: 3.d. Verification: DRC

## Slide 25: 3.d. Verification: DRC
This 3 errors can be ignored
Some special errors:
  GR134a “not touching gate”: happened in forward body bias, the VDD need to be connected to Nwell and Pwell by diode (RX layer)
  GR131_ “ratio of (area)” : when some wire is to long or wide, this kind of error for preventing the antenna violation. Use the “hop up” technique to fix that.
missing diode
N3 (Isolated Pwell for
forward biased NMOS
Can be ignored

## Slide 26: 3.d. Verification: LVS
In Layout Editing window, Calibre / Run LVS. OK for runset file
The LVS rules file: “/Tools/Library/MPW126/pdk_analog/S65/SS65/SECPDK/LR6LP/REV00/rule/LVS/CalibreLVS/CalibreLVS/LVS/L6LP_CalibreLVS_V1.5.0.9_SEC0.0.0.22/L6LP_CalibreLVS_V1.5.0.9_SEC0.0.0.22”
Then Run LVS
The result should be “smile face” without any warning
Some common errors:
  missing port: check label name in layout, they should be lbl layer
  wrong properties: check transistor W,L, finger; for R value of resistor can be ignored

## Slide 27: 3.e. RC extraction and post simulation

## Slide 28: 4. Digital design
  Digital design synthesis
  Digital simulation
  Pad insertion and pre-integration
  Place and Route (PnR)
  Chip finishing and post simulation
Front End
Back End
Function simulation (VCS)
Synthesis
(DC)
HDL code
(Verilog)
SS65 lib
simulation (VCS)
Pad insertion
PnR
post sim
GDS

## Slide 29: 4.a. Synthesis
Command: dc_shell
source script_file.tcl

## Slide 30: 4. PnR
From the working directory, start the ICC:
  /Tools/Synopsys/ICC_2013.03/bin/icc_shell
In SS65nm PnR with ICC includes 9 steps
Read design
floorplan
Power plan
Placement
clock tree synthesis
post CTS opt.
netlist
Lib
.tdf
pin/pad physical constraints
Routing
Rout opt.
Finishing
.gds
.v

## Slide 31: 4. PnR - Read design
The input of “back end” is the results of “front end”:
  netlist (.v)
  standard delay constrain (.sdc)
Config ICC by modify scripts in user_scripts
To read design, in IC shell, run 00_read_design.tcl script file
source ./script/00_read_design.tcl > log_SS00.log

## Slide 32: 4. PnR – Floorplan
In Floorplan, we decide
  Core area
  Position of IO pads (load tdf script)
  Position of each block
After modify, in IC shell, run 01_floorplan.tcl script file
IO Pads and Power rings
Core
Digital
memory
Digital
analog

## Slide 33: 4. PnR – Powerplan
Define power connection between IO pad and power domain
Digital
VDDT
VDDI
VSS
IO
VDD_io (IO and digital core share power domain)

## Slide 34: 4. PnR – Powerplan
The pin CI of input pad, CD0,CD1,CE of ouput pad, and CLTCH of all pad have to connect to power domain manually
Digital
VDDT
VDDI
VSS
IO
VDD_io (IO and digital core share power domain)
In netlist _pad.v that pin have to be keep floating, however, after synthesis (using DC) that pins will automatic connect to ‘1’ or ‘0’  we need remove manually

## Slide 35: 4. PnR – Powerplan
Define multiple power domain (if need)
Digital
VDDT
VDDI
VSS
IO
VDD_io (IO and digital core share power domain)
E1
E2

## Slide 36: 4. PnR – Powerplan
Make power ring
Core
VDDT
VDDI
VSS
IO

## Slide 37: 4. PnR – Powerplan
Define route guide
IO Pads and Power rings
Core
Digital
memory
Digital
analog
Only using M1, M2, M3 for signal routing in this area
No routing in this area

## Slide 38: 4. PnR – Other step
In IC shell, run script files:
03_place_opt.tcl
04_clock_opt_cts.tcl
05_clock_opt_psyn.tcl
06_route.tcl
07_route_opt.tcl
08_chip_finish.tcl

## Slide 39: 4.e. Error handle
Error browsing: In IC compiler layout window, select Verification/Error browser. Choose “Detail route” then click OK

## Slide 40: 4.e. Error handle
In digital design’s PnR, some critical violations:
  short circuit
  Diff/Same net spacing
Some clues:
  Search and repair
  Repartitioning (in floorplan)
  Change cell density
  Change placement and optimization option

## Slide 41: 4.e. Error handle
For antenna violation fixing: Route/Detail routing  Set Detail route option … Modify those option to getting the best result.
In some case, antenna violation can not be fixed completely, they should be fix manually by hop up techinique (detail in section 5)

## Slide 42: 5. Mixed-signal design

## Slide 43: 5.a. Preparing
  This guideline is for manual integration without timing verification.
  The full-custom blocks (macros) will be embedded into chip’s layout after PnR step of digital part.
  Preparing:
    macro’s size, pins position
    Macro’s position (floorplan)
    Power for macro
IO Pads and Power rings
Core
Analog or Memory Macro
Digital

## Slide 44: IO pad
IO Pads and Power rings
Core
Analog Macro
VDDT power pad (3.3V)
VDDI power pad (1.2V)
GND pad
Analog pad
Digital IO pad
breaker
VDDI power pad
Memory or full custom digital Macro
VDDI power pad
Digital

## Slide 45: IO pad
Position of pad is defined in padplace.tdf file
IDEC provide a standard padplace file. If we want to do bonding in IDEC, do not change the offset position
IO Pads and Power rings
(0,0)
left
top
right
bottom
Pad 1
Pad 208
offset

## Slide 46: IO pad
Add breaker to isolate power domains
IO Pads and Power rings
(0,0)
Pad 1
Pad 208
Define pin's position of macros
Macro

## Slide 47: 5.b. PnR
In general, PnR for mixed design is similar with PnR for digital design. But we need some specific setup for macros
  Floorplan:
  Power and Pre-route:
IO Pads and Power rings
Macro
Digital

## Slide 48: 5.b. PnR: Common violation
After PnR, you will meet a lot of violation related to:
  short circuit: check detail one by one, if error due to the pins (for connection with custom modules), that can be ignore.
  antenna: can be fixed by:
    diode insertion
    hop up
    manual hop up (during merging step)
  Diff net spacing:
    check the pins connection.
    if impossible to fix manually, run “fix and route” again
  Same net spacing: if impossible to fix manually, run “fix and route” again
  Non-preferred … : ignore
for understanding antenna violation: http://www.edn.com/design/integrated-circuit-design/4440143/Antenna-violations-resolved-using-new-method

## Slide 49: Layout merging
In the 08_chip_finish, output of PnR is a layout file .gds
In virtuoso, import that gds file

## Slide 50: 6. Stream in/out
Stream out: export layout to GDS file
From CIW window, File/Export/Stream

## Slide 51: 6. Stream in/out
Load tech map file.
Then “Translate”

## Slide 52: 6. Stream in/out
Stream in: import layout to Virtuoso
From CIW window, File/Import/Stream

## Slide 53: 6. Stream in/out
Choose the gds file to be import
load the tech map file (same as stream out process)
Name the imported library (new name)
Put the top cell name
Choose the tech lib: l6lp_tech
“Translate”

## Slide 54: 7. Merging
Have fun in IDEC!