## Slide 1
Motion detect processor
Dang Le Dinh Trang

## Slide 2
System diagram
PC
(Qt app on Ubuntu)
FPGA (DE2-115)
MPR121
UART
I2C
UART
Controller
I2C controller
SPI master controller
ADS1292
SPI

## Slide 3
PC app
OS: Ubuntu/Window
Dev platform: Qt
Features for MPR:
  Read/write registers
  Auto read touch results
Features for ADS:
  Send system command
  Receive and show ECG data stream continue

## Slide 4: UART
Console
Test connection between PC and FPGA. If connection is ok, console will show “54 54 54 …”
Close program

## Slide 5
Connect with FPGA by serial port
Click to “Setting” of UART fpga
Select serial port
Baudrate = 115200
Apply
Then click to Connect on mainwindow

## Slide 6
MPR121 control
Touch results of 12 channel
1 is touched
0 is none
Start sensing
Stop sensing
Register address
Written value
Read/write register

## Slide 7: MPR121 testing
Connect FPGA via UART
Click Start for start sensing
Click Stop for stop sensing
For individual configure or access any MPR’s register, read/write with address and a value
MPR121 | DE2-115
IRQ | GPIO_23
SCL | GPIO_22
SDA | GPIO_25
ADDR | GPIO_24
GND | GND
VIN | 5V

## Slide 8: ADS1292
select register
select system command
Value for write into reg
ECG waveform (raw data)

## Slide 9: ADS1292 testing
After connect PC
Click Auto config
Click Read data continue for start measurement and receive ECG data
Click ADS read or Auto config for stop
ADS1292 | DE2-115
VCC | 3.3V
SPI_CLK | GPIO_17
SPI_MISO | GPIO_14
SPI_MOSI | GPIO_15
DRDY | GPIO_12
RESET | GPIO_13
START | GPIO_10
SPI_CSN | GPIO_11
DGND | GND

## Slide 10
Source code
FPGA code: khu_sensor.tar.gz
PC app source code: khu_sensor_test.tar.gz