## Modules

## khu_sensor_top
'khu_sensor_top' module assigns pins of fpga to parameters. The parameters are used to communicate with ADS1292(SPI), MPR121(I2C), PC(UART).

## ads1292_controller
'ads1292_controller' module directly communicates with ADS1292 sensor through spi_master. States are defined in this module, and parameters are set valid to each state. The parameters defiend by reference/ADS1292/ADS1292.pdf.

### Input Port

* i_CLK
  * 50MHz

* i_RSTN
  * It is pulled low when reset button(KEY[0]) is clicked.

* [2:0] i_ADS1292_CONTROL : Decide ADS1292's mode
  * 3'b000 -> IDLE mode
  * 3'b001 -> SYSCMD mode
  * 3'b010 -> WREG mode
  * 3'b011 -> RREG mode
  * 3'b100 -> RDATAC mode
  * 3'b101 -> SDATAC mode
  * 3'b111 -> DUMMY mode

* [7:0] i_ADS1292_COMMAND : Defined opcode command for setting ADS's state
  * 8'h06 -> RESET
  * 8'h08 -> START
  * 8'h0A -> STOP
  * 8'h10 -> RDATAC
  * 8'h11 -> SDATAC

* [7:0] i_ADS1292_REG_ADDR : Register address to write or read data
  * 8'h01 -> CONFIG1
  * 8'h02 -> CONFIG2
  * 8'h03 -> LOFF
  * 8'h04 -> CH1SET
  * 8'h05 -> CH2SET
  * 8'h06 -> RLD_SENS
  * 8'h07 -> LOFF_SENS
  * 8'h08 -> LOFF_STAT
  * 8'h09 -> RESP1
  * 8'h0A -> RESP2
  * 8'h0B -> GPIO

* [7:0] i_ADS1292_DATA_IN : Register data to be written in specific register
  * 8'h01 -> written in CONFIG1
  * 8'hE0 -> written in CONFIG2
  * 8'h10 -> written in LOFF
  * 8'h00 -> written in CH1SET
  * 8'h00 -> written in CH2SET
  * 8'h2C -> written in RLD_SENS
  * 8'h0E -> written in vLOFF_SENS
  * 8'h00 -> written in LOFF_STAT
  * 8'h02 -> written in RESP1
  * 8'h87 -> written in RESP2
  * 8'h00 -> written in GPIO

* i_SPI_MISO : 1bit data that ADS1292 sends to DE2-115
  * Written data of register : In RREG mode
  * Conversion data (1bit out of 72bit) : In RDATAC mode

* i_ADS1292_DRDY : 1bit data that ADS1292 sends to DE2-115 when conversion data ready
  * First 1'b0 -> 1'b1 : Go High with start pin
  * First 1'b1 -> 1'b0 : Conversion data is ready
  * Second 1'b0 -> 1'b1 : Output conversion data

### Output Port

* reg [71:0] o_ADS1292_DATA_OUT
  * In RDATAC mode, a set of 1'bit i_SPI_MISO data.

* reg o_ADS1292_INIT_SET
  * It is pulled high when ADS1292 wait for power-on reset.

* reg o_ADS1292_DATA_READY
  * In RDATAC mode, it goes high when 72bit conversion data are ready

* reg o_ADS1292_BUSY
  * It goes high when ADS1292 operates in a particular mode.

* reg o_ADS1292_FAIL

* [15:0] o_ads_reg_c
  * In RREG mode, o_ads_reg_c is the combination of r_ads_reg_a and r_ads_reg_b.
r_ads_reg_a is register address to read.
r_ads_reg_b is (number of registers to read at the same time) -1.

    * Example
If you want read CONFIG1, CONFIG2, LOFF at the same time, o_ads_reg_c <= 0010000100000010.
If you want read LOFF only, o_ads_reg_c <= 0010001100000000

* o_SPI_CLK
  * SCLK determined by CLKS_PER_HALF_BIT is assigned this port.
  * CLKS_PER_HALF_BIT is 25, so o_SPI_CLK <= 1MHz (50M / (25 * 2))

* o_SPI_MOSI
  * It is 1bit piece of bits that DE2-115 sends to ADS1292, including opcode, register addree etc.

* reg o_ADS1292_RESET
  * It is pulled high at idle mode, power on reset state.

* reg o_ADS1292_START
  * It goes high when start pin is pulled high or in RDATAC mode.

* reg o_SPI_CSN
  * It remain low when ADS1292 communicate with master.
It goes high in idle mode or waiting specific state.

## sensor_core
### Input
##### UART Controller
* i_UART_DATA_TX_READY
  * 1'b1: either MPR121 or ADS1292 fully received Bio-signal
* i_UART_DATA_RX[15:8]
  * 8'h6D : read setted data from MPR reg address **i_UART_DATA_RX[7:0]**
  * 8'h61 : read setted data from ADS reg address **i_UART_DATA_RX[7:0]**
  * 8'h52 : Alternately get bio_signal from MPR and ADS
  * 8'h53 : stop getting bio_signal from MPR and ADS
  * __8'h46 : ???__
  * __8'h66 : ???__
* i_UART_DATA_RX_VALID
  * 1'b1: FPGA fully recieved single byte info from UART

##### MPR121
* i_MPR121_DATA_OUT[7:0]
  * alternately recieve touch status from sensor **0~7** and **8~11**
* i_MPR121_INIT_SET
  * 1'b1 : initiation code successfully passed to MPR
* i_MPR121_BUSY
  * 1'b1 : MPR either on WRITE or READ state
* i_MPR121_FAIL
  * 1'b1 : unexpected error occured during process

##### ADS1292
* i_ADS1292_DATA_OUT
  * i_ADS1292_DATA_OUT[71:48] : ADS status data
  * i_ADS1292_DATA_OUT[47:24] ; ADS CH1 data
  * i_ADS1292_DATA_OUT[23:0] : ADS CH2 data
* i_ADS1292_INIT_SET
  * 1'b1 : initiation code successfully passed to ADS
* i_ADS1292_DATA_READY
  * 1'b1 : **i_ADS1292_DATA_OUT[71:0]** are ready to be passed by ADS
* i_ADS1292_BUSY
  * 1'b1 : ADS either on WRITE or READ state
* i_ADS1292_FAIL
  * 1'b1 : unexpected error occured during process

##### System I/O
* i_CLK : 25MHz clock
* i_RST
   * 1'b1 : reset all process

### Output
##### UART Controller
* o_UART_DATA_TX
  * o_UART_DATA_TX[79:72]

* o_UART_DATA_TX_VALID
   * 1'b1 : 80bit data are fully recieved

##### MPR121
* o_MPR121_REG_ADDR[7:0] : specific register address of MPR to write or read
* o_MPR121_DATA_IN[7:0] : data to write on specific MPR address
* o_MPR121_WRITE_ENABLE
  * 1'b1 : order MPR to be on write state
* o_MPR121_READ_ENABLE
  * 1'b1 : order MPR to be on data recieve state

##### System connection with MPR121 data
* o_MPR121_TOUCH_STATUS
  * o_MPR121_TOUCH_STATUS[11:8] : touch sensor 8~11 status
  * o_MPR121_TOUCH_STATUS[7:0] : touch sensor 0~7 status
* o_MPR121_ERROR
  * 1'b1: LEDR[16] light on

##### ADS1292
* o_ADS1292_CONTROL [2:0]
  * 3'b001 : ADS on system command mode
  * 3'b010 : ADS on write register mode
  * 3'b011 : ADS on read register mode
  * 3'b100 : ADS on read data continuously mode
  * 3'b101 : ADS on stop data continuously mode
  * 3'b111 : ADS on send dummy mode
* o_ADS1292_COMMAND [7:0] : send user defined command according to **o_ADS1292_CONTROL[2:0]**
* o_ADS1292_REG_ADDR [7:0] : specific register address of ADS to write or read
* o_ADS1292_DATA_IN[ [7:0] : data to write on specific ADS address

##### System I/O
* o_CHIP_SET
  * 1'b1 : both MPR and ADS chip set done
* o_RUN_SET
  * 1'b1 : both MPR and ADS run set done
* o_CORE_BUSY
  * 1'b1 : both MPR and ADS on reading data state

## uart_controller

## sensor_core.v
### Input
##### UART Controller
* i_UART_DATA_TX_READY
  * 1'b1: either MPR121 or ADS1292 fully received Bio-signal
* i_UART_DATA_RX[15:8]
  * 8'h6D : read setted data from MPR reg address **i_UART_DATA_RX[7:0]**
  * 8'h61 : read setted data from ADS reg address **i_UART_DATA_RX[7:0]**
  * 8'h52 : Alternately get bio_signal from MPR and ADS
  * 8'h53 : stop getting bio_signal from MPR and ADS
  * __8'h46 : ???__
  * __8'h66 : ???__
* i_UART_DATA_RX_VALID
  * 1'b1: FPGA fully recieved single byte info from UART

##### MPR121
* i_MPR121_DATA_OUT[7:0]
  * alternately recieve touch status from sensor **0~7** and **8~11**
* i_MPR121_INIT_SET
  * 1'b1 : initiation code successfully passed to MPR
* i_MPR121_BUSY
  * 1'b1 : MPR either on WRITE or READ state
* i_MPR121_FAIL
  * 1'b1 : unexpected error occured during process

##### ADS1292
* i_ADS1292_DATA_OUT
  * i_ADS1292_DATA_OUT[71:48] : ADS status data
  * i_ADS1292_DATA_OUT[47:24] ; ADS CH1 data
  * i_ADS1292_DATA_OUT[23:0] : ADS CH2 data
* i_ADS1292_INIT_SET
  * 1'b1 : initiation code successfully passed to ADS
* i_ADS1292_DATA_READY
  * 1'b1 : **i_ADS1292_DATA_OUT[71:0]** are ready to be passed by ADS
* i_ADS1292_BUSY
  * 1'b1 : ADS either on WRITE or READ state
* i_ADS1292_FAIL
  * 1'b1 : unexpected error occured during process

##### System I/O
* i_CLK : 25MHz clock
* i_RST
   * 1'b1 : reset all process

### Output
##### UART Controller
* o_UART_DATA_TX
  * o_UART_DATA_TX[79:72]
    * 8'hBB : send MPR sensor data
    * 8'hAA : send ADS sensor data
    * 8'h6D : send MPR register data
    * 8'h61 : send ADS register data
* o_UART_DATA_TX_VALID
   * 1'b1 : 80bit data are fully recieved

##### MPR121
* o_MPR121_REG_ADDR[7:0] : specific register address of MPR to write or read
* o_MPR121_DATA_IN[7:0] : data to write on specific MPR address
* o_MPR121_WRITE_ENABLE
  * 1'b1 : order MPR to be on write state
* o_MPR121_READ_ENABLE
  * 1'b1 : order MPR to be on data recieve state

##### System connection with MPR121 data
* o_MPR121_TOUCH_STATUS
  * o_MPR121_TOUCH_STATUS[11:8] : touch sensor 8~11 status
  * o_MPR121_TOUCH_STATUS[7:0] : touch sensor 0~7 status
* o_MPR121_ERROR
  * 1'b1: LEDR[16] light on

##### ADS1292
* o_ADS1292_CONTROL [2:0]
  * 3'b001 : ADS on system command mode
  * 3'b010 : ADS on write register mode
  * 3'b011 : ADS on read register mode
  * 3'b100 : ADS on read data continuously mode
  * 3'b101 : ADS on stop data continuously mode
  * 3'b111 : ADS on send dummy mode
* o_ADS1292_COMMAND [7:0] : send user defined command according to **o_ADS1292_CONTROL[2:0]**
* o_ADS1292_REG_ADDR [7:0] : specific register address of ADS to write or read
* o_ADS1292_DATA_IN[ [7:0] : data to write on specific ADS address

##### System I/O
* o_CHIP_SET
  * 1'b1 : both MPR and ADS chip set done
* o_RUN_SET
  * 1'b1 : both MPR and ADS run set done
* o_CORE_BUSY
  * 1'b1 : both MPR and ADS on reading data state

## Prerequisites

- Quartus II (Version 15.0)
- DE2-115 Board (Cyclone IV E, EP4CE115F29C7)
- MPR121 (Touch Sensor)
- ADS1292 (ECG Sensors)

## BlockDiagram
![Block Diagram](khu_sensor_blockdiagram.png)

## Modules

## khu_sensor_top
'khu_sensor_top' module assigns pins of fpga to parameters. The parameters are used to communicate with ADS1292(SPI), MPR121(I2C), PC(UART).

## ads1292_controller
'ads1292_controller' module directly communicates with ADS1292 sensor through spi_master. States are defined in this module, and parameters are set valid to each state. The parameters defiend by reference/ADS1292/ADS1292.pdf.

### Input Port

* i_CLK
  * 50MHz

* i_RSTN
  * It is pulled low when reset button(KEY[0]) is clicked.

* [2:0] i_ADS1292_CONTROL : Decide ADS1292's mode
  * 3'b000 -> IDLE mode
  * 3'b001 -> SYSCMD mode
  * 3'b010 -> WREG mode
  * 3'b011 -> RREG mode
  * 3'b100 -> RDATAC mode
  * 3'b101 -> SDATAC mode
  * 3'b111 -> DUMMY mode

* [7:0] i_ADS1292_COMMAND : Defined opcode command for setting ADS's state
  * 8'h06 -> RESET
  * 8'h08 -> START
  * 8'h0A -> STOP
  * 8'h10 -> RDATAC
  * 8'h11 -> SDATAC

* [7:0] i_ADS1292_REG_ADDR : Register address to write or read data
  * 8'h01 -> CONFIG1
  * 8'h02 -> CONFIG2
  * 8'h03 -> LOFF
  * 8'h04 -> CH1SET
  * 8'h05 -> CH2SET
  * 8'h06 -> RLD_SENS
  * 8'h07 -> LOFF_SENS
  * 8'h08 -> LOFF_STAT
  * 8'h09 -> RESP1
  * 8'h0A -> RESP2
  * 8'h0B -> GPIO

* [7:0] i_ADS1292_DATA_IN : Register data to be written in specific register
  * 8'h01 -> written in CONFIG1
  * 8'hE0 -> written in CONFIG2
  * 8'h10 -> written in LOFF
  * 8'h00 -> written in CH1SET
  * 8'h00 -> written in CH2SET
  * 8'h2C -> written in RLD_SENS
  * 8'h0E -> written in vLOFF_SENS
  * 8'h00 -> written in LOFF_STAT
  * 8'h02 -> written in RESP1
  * 8'h87 -> written in RESP2
  * 8'h00 -> written in GPIO

* i_SPI_MISO : 1bit data that ADS1292 sends to DE2-115
  * Written data of register : In RREG mode
  * Conversion data (1bit out of 72bit) : In RDATAC mode

* i_ADS1292_DRDY : 1bit data that ADS1292 sends to DE2-115 when conversion data ready
  * First 1'b0 -> 1'b1 : Go High with start pin
  * First 1'b1 -> 1'b0 : Conversion data is ready
  * Second 1'b0 -> 1'b1 : Output conversion data

### Output Port

* reg [71:0] o_ADS1292_DATA_OUT
  * In RDATAC mode, a set of 1'bit i_SPI_MISO data.

* reg o_ADS1292_INIT_SET
  * It is pulled high when ADS1292 wait for power-on reset.

* reg o_ADS1292_DATA_READY
  * In RDATAC mode, it goes high when 72bit conversion data are ready

* reg o_ADS1292_BUSY
  * It goes high when ADS1292 operates in a particular mode.

* reg o_ADS1292_FAIL

* [15:0] o_ads_reg_c
  * In RREG mode, o_ads_reg_c is the combination of r_ads_reg_a and r_ads_reg_b.
r_ads_reg_a is register address to read.
r_ads_reg_b is (number of registers to read at the same time) -1.

    * Example
If you want read CONFIG1, CONFIG2, LOFF at the same time, o_ads_reg_c <= 0010000100000010.
If you want read LOFF only, o_ads_reg_c <= 0010001100000000

* o_SPI_CLK
  * SCLK determined by CLKS_PER_HALF_BIT is assigned this port.
  * CLKS_PER_HALF_BIT is 25, so o_SPI_CLK <= 1MHz (50M / (25 * 2))

* o_SPI_MOSI
  * It is 1bit piece of bits that DE2-115 sends to ADS1292, including opcode, register addree etc.

* reg o_ADS1292_RESET
  * It is pulled high at idle mode, power on reset state.

* reg o_ADS1292_START
  * It goes high when start pin is pulled high or in RDATAC mode.

* reg o_SPI_CSN
  * It remain low when ADS1292 communicate with master.
It goes high in idle mode or waiting specific state.

## sensor_core
### Input
##### UART Controller
* i_UART_DATA_TX_READY
  * 1'b1: either MPR121 or ADS1292 fully received Bio-signal
* i_UART_DATA_RX[15:8]
  * 8'h6D : read setted data from MPR reg address **i_UART_DATA_RX[7:0]**
  * 8'h61 : read setted data from ADS reg address **i_UART_DATA_RX[7:0]**
  * 8'h52 : Alternately get bio_signal from MPR and ADS
  * 8'h53 : stop getting bio_signal from MPR and ADS
  * __8'h46 : ???__
  * __8'h66 : ???__
* i_UART_DATA_RX_VALID
  * 1'b1: FPGA fully recieved single byte info from UART

##### MPR121
* i_MPR121_DATA_OUT[7:0]
  * alternately recieve touch status from sensor **0~7** and **8~11**
* i_MPR121_INIT_SET
  * 1'b1 : initiation code successfully passed to MPR
* i_MPR121_BUSY
  * 1'b1 : MPR either on WRITE or READ state
* i_MPR121_FAIL
  * 1'b1 : unexpected error occured during process

##### ADS1292
* i_ADS1292_DATA_OUT
  * i_ADS1292_DATA_OUT[71:48] : ADS status data
  * i_ADS1292_DATA_OUT[47:24] ; ADS CH1 data
  * i_ADS1292_DATA_OUT[23:0] : ADS CH2 data
* i_ADS1292_INIT_SET
  * 1'b1 : initiation code successfully passed to ADS
* i_ADS1292_DATA_READY
  * 1'b1 : **i_ADS1292_DATA_OUT[71:0]** are ready to be passed by ADS
* i_ADS1292_BUSY
  * 1'b1 : ADS either on WRITE or READ state
* i_ADS1292_FAIL
  * 1'b1 : unexpected error occured during process

##### System I/O
* i_CLK : 25MHz clock
* i_RST
   * 1'b1 : reset all process

### Output
##### UART Controller
* o_UART_DATA_TX
  * o_UART_DATA_TX[79:72]
    * 8'hBB : send MPR sensor data
    * 8'hAA : send ADS sensor data
    * 8'h6D : send MPR register data
    * 8'h61 : send ADS register data
* o_UART_DATA_TX_VALID
   * 1'b1 : 80bit data are fully recieved

##### MPR121
* o_MPR121_REG_ADDR[7:0] : specific register address of MPR to write or read
* o_MPR121_DATA_IN[7:0] : data to write on specific MPR address
* o_MPR121_WRITE_ENABLE
  * 1'b1 : order MPR to be on write state
* o_MPR121_READ_ENABLE
  * 1'b1 : order MPR to be on data recieve state

##### System connection with MPR121 data
* o_MPR121_TOUCH_STATUS
  * o_MPR121_TOUCH_STATUS[11:8] : touch sensor 8~11 status
  * o_MPR121_TOUCH_STATUS[7:0] : touch sensor 0~7 status
* o_MPR121_ERROR
  * 1'b1: LEDR[16] light on

##### ADS1292
* o_ADS1292_CONTROL [2:0]
  * 3'b001 : ADS on system command mode
  * 3'b010 : ADS on write register mode
  * 3'b011 : ADS on read register mode
  * 3'b100 : ADS on read data continuously mode
  * 3'b101 : ADS on stop data continuously mode
  * 3'b111 : ADS on send dummy mode
* o_ADS1292_COMMAND [7:0] : send user defined command according to **o_ADS1292_CONTROL[2:0]**
* o_ADS1292_REG_ADDR [7:0] : specific register address of ADS to write or read
* o_ADS1292_DATA_IN[ [7:0] : data to write on specific ADS address

##### System I/O
* o_CHIP_SET
  * 1'b1 : both MPR and ADS chip set done
* o_RUN_SET
  * 1'b1 : both MPR and ADS run set done
* o_CORE_BUSY
  * 1'b1 : both MPR and ADS on reading data state

## uart_controller

## sensor_core.v
### Input
##### UART Controller
* i_UART_DATA_TX_READY
  * 1'b1: either MPR121 or ADS1292 fully received Bio-signal
* i_UART_DATA_RX[15:8]
  * 8'h6D : read setted data from MPR reg address **i_UART_DATA_RX[7:0]**
  * 8'h61 : read setted data from ADS reg address **i_UART_DATA_RX[7:0]**
  * 8'h52 : Alternately get bio_signal from MPR and ADS
  * 8'h53 : stop getting bio_signal from MPR and ADS
  * __8'h46 : ???__
  * __8'h66 : ???__
* i_UART_DATA_RX_VALID
  * 1'b1: FPGA fully recieved single byte info from UART

##### MPR121
* i_MPR121_DATA_OUT[7:0]
  * alternately recieve touch status from sensor **0~7** and **8~11**
* i_MPR121_INIT_SET
  * 1'b1 : initiation code successfully passed to MPR
* i_MPR121_BUSY
  * 1'b1 : MPR either on WRITE or READ state
* i_MPR121_FAIL
  * 1'b1 : unexpected error occured during process

##### ADS1292
* i_ADS1292_DATA_OUT
  * i_ADS1292_DATA_OUT[71:48] : ADS status data
  * i_ADS1292_DATA_OUT[47:24] ; ADS CH1 data
  * i_ADS1292_DATA_OUT[23:0] : ADS CH2 data
* i_ADS1292_INIT_SET
  * 1'b1 : initiation code successfully passed to ADS
* i_ADS1292_DATA_READY
  * 1'b1 : **i_ADS1292_DATA_OUT[71:0]** are ready to be passed by ADS
* i_ADS1292_BUSY
  * 1'b1 : ADS either on WRITE or READ state
* i_ADS1292_FAIL
  * 1'b1 : unexpected error occured during process

##### System I/O
* i_CLK : 25MHz clock
* i_RST
   * 1'b1 : reset all process

### Output
##### UART Controller
* o_UART_DATA_TX
  * o_UART_DATA_TX[79:72]
    * 8'hBB : send MPR sensor data
    * 8'hAA : send ADS sensor data
    * 8'h6D : send MPR register data
    * 8'h61 : send ADS register data
* o_UART_DATA_TX_VALID
   * 1'b1 : 80bit data are fully recieved

##### MPR121
* o_MPR121_REG_ADDR[7:0] : specific register address of MPR to write or read
* o_MPR121_DATA_IN[7:0] : data to write on specific MPR address
* o_MPR121_WRITE_ENABLE
  * 1'b1 : order MPR to be on write state
* o_MPR121_READ_ENABLE
  * 1'b1 : order MPR to be on data recieve state

##### System connection with MPR121 data
* o_MPR121_TOUCH_STATUS
  * o_MPR121_TOUCH_STATUS[11:8] : touch sensor 8~11 status
  * o_MPR121_TOUCH_STATUS[7:0] : touch sensor 0~7 status
* o_MPR121_ERROR
  * 1'b1: LEDR[16] light on

##### ADS1292
* o_ADS1292_CONTROL [2:0]
  * 3'b001 : ADS on system command mode
  * 3'b010 : ADS on write register mode
  * 3'b011 : ADS on read register mode
  * 3'b100 : ADS on read data continuously mode
  * 3'b101 : ADS on stop data continuously mode
  * 3'b111 : ADS on send dummy mode
* o_ADS1292_COMMAND [7:0] : send user defined command according to **o_ADS1292_CONTROL[2:0]**
* o_ADS1292_REG_ADDR [7:0] : specific register address of ADS to write or read
* o_ADS1292_DATA_IN[ [7:0] : data to write on specific ADS address

##### System I/O
* o_CHIP_SET
  * 1'b1 : both MPR and ADS chip set done
* o_RUN_SET
  * 1'b1 : both MPR and ADS run set done
* o_CORE_BUSY
  * 1'b1 : both MPR and ADS on reading data state

 -***Italic***: module name

 -**Bold**: reg or wire name

![screensh](./reference/Image/khu_sensor_blockdiagram.png)

# Content

# Module Detail

## UART

- - -

### my_pll.v

- - -

designed phase locked loop

* input: 50M clock

* output: 5M, 25M, 100M clock

- - -

### uart_controller.v

* input clock: 25M - tried to match with MPR's clock 25M

* baud rate: 115200

* UART_CLKS_PER_BIT: 25M/115200 = 217

##### - LUT FOR uart_controller.v

|Parameters|hex|definition|
|---:|---:|---:|
|UART_SG_RUN|8'h52|Turn devices on |
|UART_SG_STOP|8'h53|Turn devices off|
|UART_SG_ADS_FINISH|8'h46| ADS Data ready|
|UART_SG_ADS_READ_REG|8'h61| ADS Register read|

##### - LUT FOR uart_controller state

|State|hex|definiton|
|---:|---|---|
|ST_IDLE|8'd0| checking 'w_uart_data_Rx' stage|
|ST_RX_READ_REG_ADDR|8'd4| PC wants to read REG, so concentrate two 'w_uart_data_Rx'|

> uart_controller.v verifies data sent from PC

### uart_tx.v

* **i_UART_DATA_TX_VALID** bit high(1) will initiate uart_tx

* In our case there are two types of tx data
  * **40Bits** : when header is **ADS_SEND_DATA**
  * **24Bits** : when header is **MPR_SEND_DATA, ADS_READ_DATA, MPR_READ_DATA**

* The only different of two case is how many reps uart_tx has to repeat.(uart can send or receive 8 bits at once)

* So, from [39:32] to [7:0] start sending it by giving signal **r_uart_data_tx_valid** high(1)
  * **r_uart_data_tx_valid** : data setting for uart tx is ready, begin uart_tx communication

* **o_Tx_Active** : always goes high(1) during communication

* **o_Tx_Serial** : single bit data that really sent to PC. consisting **r_Tx_Data's ** from LSB to MSB
### uart_rx.v

* **i_Rx_Serial** (i_UART_RXD==UART_RXD) inputs low to begin ***UART_RX***

* After two cycle **i_Rx_Serial(i_UART_RXD)** replicated to **r_Rx_Data**

* When **r_Clock_count** reaches (CLKS_PER_BIT-1)/2=108, change state to **s_RX_START_BIT**

* **r_Rx_Byte[7:0]** getting filled with **r_Rx_Data** from LSB to MSB (r_Rx_Data doesn't have to be low this time)

* After **r_Rx_Byte[7:0]** is filled, change state and wait (CLKS_PER_BIT-1) cycle

* When **r_Clock_count** reaches (CLKS_PER_BIT-1), state changes with register **r_Rx_Dv** high,

* At s_CLEANUP state change register '**r_Rx_Dv**' back to low

* assign **o_Rx_DV, O_Rx_Byte** with **r_Rx_DV, r_Rx_Byte**

|r_SM_Main(State) | s_IDLE | s_RX_START_BIT | s_RX_DATA_BITS | s_RX_STOP_BIT | s_CLEANUP |
|----------:|--------:|----------------:|----------------:|---------------:|-----------:|
|Cycle Cost|-|(CLKS_PER_BIT-1)/2|CLKS_PER_BIT * 8 |CLKS_PER_BIT|1|
|r_Rx_DV|0->0|0->0|0->0|0-><span style="color:red">1</span>|1->0|
|r_Rx_Data|0|0|1,0|1,0|1,0|
|r_Rx_Byte|00000000|00000000|hgfedcba(start from LSB)|-| -|

 >uart_rx.v send 8bit data PC send, plus makes output r_Rx_Dv high right after 1 byte is filled. goes back to 0 at next cycle

### sensor_core.v

- - -

### spi_master.v

* input clock: 50M

* spi_mode=1, (CPOL,CPHA)=(0,1)

* CLKS_PER_HALF_BIT= 49,

 - i_CLK/(CLKS_PER_HALF_BIT*2)=f_CLK=512kHz

##### MOSI
>	> as **i_TX_DV(r_spi_data_in_valid)** goes high for a moment, **r_SPI_CLK_Edges** becomes 16, **o_TX_Ready** becomes 1'b0
>	> to prevent unwanted data change, we used cycle delay

<pre>
<code>
 always @(posedge i_Clk or negedge i_Rst_L)
  begin
    if (~i_Rst_L)
    begin
      r_TX_Byte <= 8'h00;
      r_TX_DV <= 1'b0;
    end
    else
      begin
        r_TX_DV <= i_TX_DV; // 1 clock cycle delay !!!
        if (i_TX_DV)
        begin
        r_TX_Byte <= i_TX_Byte;
        end
      end
  end
</code>
</pre>

>	> after **i_TX_DV** becomes low again, make SPI it's own 16 cycle using reg **r_Trailing_Egde, r_Leading_Egde**

<p align="center">
  <img width="600" height="200" src="./reference/Image/spi_clock.PNG">
</p>

>	> now at the Edge of spi_clock send single bit of input Byte **i_TX_Byte** from MSB to LSB

<pre>
<code>
 else if ((r_Leading_Edge & w_CPHA) | (r_Trailing_Edge & ~w_CPHA))
      begin
        r_TX_Bit_Count <= r_TX_Bit_Count - 1;
        o_SPI_MOSI <= r_TX_Byte[r_TX_Bit_Count];
 end
</code>
</pre>

>	> when data(**o_MOSI**) send is done, give **o_TX_Ready** 1'b1

###### MISO

>	> When **i_TX_DV** turns to high(1'b1),ini
>	> Start filling **o_RX_Byte[7:0]** with **i_SPI_MISO[0:0]** ( will cost 7 cycle)

<pre>
<code>
 if (o_TX_Ready)
      begin
        r_RX_Bit_Count <= 3'b111;
      end
      else if ((r_Leading_Edge & ~w_CPHA) | (r_Trailing_Edge & w_CPHA))
      begin
        o_RX_Byte[r_RX_Bit_Count] <= i_SPI_MISO;
        r_RX_Bit_Count <= r_RX_Bit_Count - 1;
        if (r_RX_Bit_Count == 3'b000)
        begin
        o_RX_DV <= 1'b1; // Byte done, pulse Data Valid
        end
      end
</code>
</pre>

>	> When **o_RX_Byte** is all filled, export **o_RX_DV <= 1'b1**

### ads1292_controller.v

* input clock: 50M

* **o_ADS1292_START** : 1'b1 when ads starts, start here means when ads returns data. So at RREG or WREG command, **o_ADS1292_START** goes 1'b0

* **o_SPI_CSN** : meaning chip select, there are various chips(ex. ADS1292, ADS1291 ... ) and you can only communicate with one chip using SPI protocol.
   - After the serial communication is finished, ***always wait four or more tCLK cycles*** before taking CS high
   - When CS is taken high, the serial interface is reset(SCLK and DIN are ignored,and DOUT enters a high-impedance state)

* **i_ADS1292_DRDY** : output of ads1292, meaning new conversion data are ready

### mpr121_controller.v

### i2c_master.v

### khu_sensor_top.v(top module)

# khu_sensor

## Introduction

## Contents

* [Prerequesites](#prerequisites)
* [BlockDiagram](#BlockDiagram)
* [Modules](#Modules)
- [khu_sensor_top](#khu_sensor_top)
- [ads1292_controller](#ads1292_controller)
 + [spi_master](#spi_master)
- [mpr121_controller](#mpr121_controller)
 + [i2c_master](#i2c_master)
- [sensor_core](#sensor_core)
- [uart_controller](#uart_controller)
 + [uart_rx](#uart_rx)
 + [uart_tx](#uart_tx)
* [Reference](#Reference)

## Prerequisites

- Quartus II (Version 15.0)
- DE2-115 Board (Cyclone IV E, EP4CE115F29C7)
- MPR121 (Touch Sensor)
- ADS1292 (ECG Sensors)

## BlockDiagram
![Block Diagram](./reference/Image/khu_sensor_blockdiagram.png)

## Modules

## khu_sensor_top
'khu_sensor_top' module assigns pins of fpga to parameters. The parameters are used to communicate with ADS1292(SPI), MPR121(I2C), PC(UART).

## ads1292_controller
'ads1292_controller' module directly communicates with ADS1292 sensor through spi_master. States are defined in this module, and parameters are set valid to each state. The parameters defiend by reference/ADS1292/ADS1292.pdf.

### Input Port

* i_CLK
  * 50MHz

* i_RSTN
  * It is pulled low when reset button(KEY[0]) is clicked.

* [2:0] i_ADS1292_CONTROL : Decide ADS1292's mode
  * 3'b000 -> IDLE mode
  * 3'b001 -> SYSCMD mode
  * 3'b010 -> WREG mode
  * 3'b011 -> RREG mode
  * 3'b100 -> RDATAC mode
  * 3'b101 -> SDATAC mode
  * 3'b111 -> DUMMY mode

* [7:0] i_ADS1292_COMMAND : Defined opcode command for setting ADS's state
  * 8'h06 -> RESET
  * 8'h08 -> START
  * 8'h0A -> STOP
  * 8'h10 -> RDATAC
  * 8'h11 -> SDATAC

* [7:0] i_ADS1292_REG_ADDR : Register address to write or read data
  * 8'h01 -> CONFIG1
  * 8'h02 -> CONFIG2
  * 8'h03 -> LOFF
  * 8'h04 -> CH1SET
  * 8'h05 -> CH2SET
  * 8'h06 -> RLD_SENS
  * 8'h07 -> LOFF_SENS
  * 8'h08 -> LOFF_STAT
  * 8'h09 -> RESP1
  * 8'h0A -> RESP2
  * 8'h0B -> GPIO

* [7:0] i_ADS1292_DATA_IN : Register data to be written in specific register
  * 8'h01 -> written in CONFIG1
  * 8'hE0 -> written in CONFIG2
  * 8'h10 -> written in LOFF
  * 8'h00 -> written in CH1SET
  * 8'h00 -> written in CH2SET
  * 8'h2C -> written in RLD_SENS
  * 8'h0E -> written in LOFF_SENS
  * 8'h00 -> written in LOFF_STAT
  * 8'h02 -> written in RESP1
  * 8'h87 -> written in RESP2
  * 8'h00 -> written in GPIO

* i_SPI_MISO : 1 bit data that ADS1292 sends to DE2-115
  * Written data of register : In RREG mode
  * Conversion data (1bit out of 72bit) : In RDATAC mode

* i_ADS1292_DRDY : 1bit data that ADS1292 sends to DE2-115 when conversion data ready
  * First 1'b0 -> 1'b1 : Go High with start pin
  * First 1'b1 -> 1'b0 : Conversion data is ready
  * Second 1'b0 -> 1'b1 : Output conversion data

### Output Port

* reg [71:0] o_ADS1292_DATA_OUT
  * In RDATAC mode, a set of 1'bit i_SPI_MISO data.

* reg o_ADS1292_INIT_SET
  * It is pulled high when ADS1292 wait for power-on reset.

* reg o_ADS1292_DATA_READY
  * In RDATAC mode, it goes high when 72bit conversion data are ready

* reg o_ADS1292_BUSY
  * It goes high when ADS1292 operates in a particular mode.

* reg o_ADS1292_FAIL

* [15:0] o_ads_reg_c
  * In RREG mode, o_ads_reg_c is the combination of r_ads_reg_a and r_ads_reg_b.
r_ads_reg_a is register address to read.
r_ads_reg_b is (number of registers to read at the same time) -1.

    * Example
If you want read CONFIG1, CONFIG2, LOFF at the same time, o_ads_reg_c <= 0010000100000010.
If you want read LOFF only, o_ads_reg_c <= 0010001100000000

* o_SPI_CLK
  * SCLK determined by CLKS_PER_HALF_BIT is assigned this port.
  * CLKS_PER_HALF_BIT is 25, so o_SPI_CLK <= 1MHz (50M / (25 * 2))

* o_SPI_MOSI
  * It is 1bit piece of bits that DE2-115 sends to ADS1292, including opcode, register addree etc.

* o_ADS1292_RESET
  * It is pulled high at idle mode, power on reset state.

* o_ADS1292_START
  * It goes high when start pin is pulled high or in RDATAC mode.

* o_SPI_CSN
  * It remain low when ADS1292 communicate with master.
It goes high in idle mode or waiting specific state.

# Module Detail

## UART

- - -

### my_pll.v

- - -

designed phase locked loop

* input: 50M clock

* output: 5M, 25M, 100M clock

- - -

### uart_controller.v

* input clock: 25M - tried to match with MPR's clock 25M

* baud rate: 115200

* UART_CLKS_PER_BIT: 25M/115200 = 217

##### - LUT FOR uart_controller.v

|Parameters|hex|definition|
|---:|---:|---:|
|UART_SG_RUN|8'h52|Turn devices on |
|UART_SG_STOP|8'h53|Turn devices off|
|UART_SG_ADS_FINISH|8'h46| ADS Data ready|
|UART_SG_ADS_READ_REG|8'h61| ADS Register read|

##### - LUT FOR uart_controller state

|State|hex|definiton|
|---:|---|---|
|ST_IDLE|8'd0| checking 'w_uart_data_Rx' stage|
|ST_RX_READ_REG_ADDR|8'd4| PC wants to read REG, so concentrate two 'w_uart_data_Rx'|

> uart_controller.v verifies data sent from PC

### uart_tx.v

* **i_UART_DATA_TX_VALID** bit high(1) will initiate uart_tx

* In our case there are two types of tx data
  * **40Bits** : when header is **ADS_SEND_DATA**
  * **24Bits** : when header is **MPR_SEND_DATA, ADS_READ_DATA, MPR_READ_DATA**

* The only different of two case is how many reps uart_tx has to repeat.(uart can send or receive 8 bits at once)

* So, from [39:32] to [7:0] start sending it by giving signal **r_uart_data_tx_valid** high(1)
  * **r_uart_data_tx_valid** : data setting for uart tx is ready, begin uart_tx communication

* **o_Tx_Active** : always goes high(1) during communication

* **o_Tx_Serial** : single bit data that really sent to PC. consisting **r_Tx_Data's ** from LSB to MSB
### uart_rx.v

* **i_Rx_Serial** (i_UART_RXD==UART_RXD) inputs low to begin ***UART_RX***

* After two cycle **i_Rx_Serial(i_UART_RXD)** replicated to **r_Rx_Data**

* When **r_Clock_count** reaches (CLKS_PER_BIT-1)/2=108, change state to **s_RX_START_BIT**

* **r_Rx_Byte[7:0]** getting filled with **r_Rx_Data** from LSB to MSB (r_Rx_Data doesn't have to be low this time)

* After **r_Rx_Byte[7:0]** is filled, change state and wait (CLKS_PER_BIT-1) cycle

* When **r_Clock_count** reaches (CLKS_PER_BIT-1), state changes with register **r_Rx_Dv** high,

* At s_CLEANUP state change register '**r_Rx_Dv**' back to low

* assign **o_Rx_DV, O_Rx_Byte** with **r_Rx_DV, r_Rx_Byte**

|r_SM_Main(State) | s_IDLE | s_RX_START_BIT | s_RX_DATA_BITS | s_RX_STOP_BIT | s_CLEANUP |
|----------:|--------:|----------------:|----------------:|---------------:|-----------:|
|Cycle Cost|-|(CLKS_PER_BIT-1)/2|CLKS_PER_BIT * 8 |CLKS_PER_BIT|1|
|r_Rx_DV|0->0|0->0|0->0|0-><span style="color:red">1</span>|1->0|
|r_Rx_Data|0|0|1,0|1,0|1,0|
|r_Rx_Byte|00000000|00000000|hgfedcba(start from LSB)|-| -|

 >uart_rx.v send 8bit data PC send, plus makes output r_Rx_Dv high right after 1 byte is filled. goes back to 0 at next cycle

### sensor_core.v

- - -

### spi_master.v

* input clock: 50M

* spi_mode=1, (CPOL,CPHA)=(0,1)

* CLKS_PER_HALF_BIT= 49,

 - i_CLK/(CLKS_PER_HALF_BIT*2)=f_CLK=512kHz

##### MOSI
>	> as **i_TX_DV(r_spi_data_in_valid)** goes high for a moment, **r_SPI_CLK_Edges** becomes 16, **o_TX_Ready** becomes 1'b0
>	> to prevent unwanted data change, we used cycle delay

<pre>
<code>
 always @(posedge i_Clk or negedge i_Rst_L)
  begin
    if (~i_Rst_L)
    begin
      r_TX_Byte <= 8'h00;
      r_TX_DV <= 1'b0;
    end
    else
      begin
        r_TX_DV <= i_TX_DV; // 1 clock cycle delay !!!
        if (i_TX_DV)
        begin
        r_TX_Byte <= i_TX_Byte;
        end
      end
  end
</code>
</pre>

>	> after **i_TX_DV** becomes low again, make SPI it's own 16 cycle using reg **r_Trailing_Egde, r_Leading_Egde**

<p align="center">
  <img width="600" height="200" src="./reference/Image/spi_clock.PNG">
</p>

>	> now at the Edge of spi_clock send single bit of input Byte **i_TX_Byte** from MSB to LSB

<pre>
<code>
 else if ((r_Leading_Edge & w_CPHA) | (r_Trailing_Edge & ~w_CPHA))
      begin
        r_TX_Bit_Count <= r_TX_Bit_Count - 1;
        o_SPI_MOSI <= r_TX_Byte[r_TX_Bit_Count];
 end
</code>
</pre>

>	> when data(**o_MOSI**) send is done, give **o_TX_Ready** 1'b1

###### MISO

>	> When **i_TX_DV** turns to high(1'b1),ini
>	> Start filling **o_RX_Byte[7:0]** with **i_SPI_MISO[0:0]** ( will cost 7 cycle)

<pre>
<code>
 if (o_TX_Ready)
      begin
        r_RX_Bit_Count <= 3'b111;
      end
      else if ((r_Leading_Edge & ~w_CPHA) | (r_Trailing_Edge & w_CPHA))
      begin
        o_RX_Byte[r_RX_Bit_Count] <= i_SPI_MISO;
        r_RX_Bit_Count <= r_RX_Bit_Count - 1;
        if (r_RX_Bit_Count == 3'b000)
        begin
        o_RX_DV <= 1'b1; // Byte done, pulse Data Valid
        end
      end
</code>
</pre>

>	> When **o_RX_Byte** is all filled, export **o_RX_DV <= 1'b1**

### ads1292_controller.v

* input clock: 50M

* **o_ADS1292_START** : 1'b1 when ads starts, start here means when ads returns data. So at RREG or WREG command, **o_ADS1292_START** goes 1'b0

* **o_SPI_CSN** : meaning chip select, there are various chips(ex. ADS1292, ADS1291 ... ) and you can only communicate with one chip using SPI protocol.
   - After the serial communication is finished, ***always wait four or more tCLK cycles*** before taking CS high
   - When CS is taken high, the serial interface is reset(SCLK and DIN are ignored,and DOUT enters a high-impedance state)

* **i_ADS1292_DRDY** : output of ads1292, meaning new conversion data are ready

### mpr121_controller.v

### i2c_master.v

### khu_sensor_top.v(top module)